## Slide 1
Indorama ventures
BENCHMARKING POLYMER PUMPS/ CHIPS CUTTERS

## Slide 2: POLYMER PUMPS BENCHMARKING
POLYMER PUMPS DATA
OBSERVATION
CONCLUSION AND PATH FORWARD

## Slide 3: POLYMER PUMPS

## Slide 4: POLYMER PUMPS

## Slide 5: POLYMER PUMPS

## Slide 6: OBSERVATION PRE-POLYMER PUMPS
THERMOREX RT 90
THERMOREX RT 140
For 180 size different models used at various sites .
APT CP1 / APT CP2 / IPPI have these pumps of same capacity installed but all 3 have different seal type VISLIP / VISPAC / DOUBLE MECHANICAL SEAL BACK TO BACK.
Also the KW rating of motors is different ? 22 KW APT CP1 / 11 KW APT CP2 / 15 KW IPPI.
IPPI has shown yearly expenses on 5400 USD for seal parts whereas APT CP-2 has NIL & APT CP-1 has 1300 USD per year .
** VISPAC technically is the best as low seal failures compared to other 2 . Double mech seal has more failures.
SPT CP2 / IVC TURKEY / IVPM use these pumps
THERMOREX RT 140 / MPS GEAR PUMP thermorex® TRP140-5 / Therminox 140/140 model used at above sites.
Seal Type is VISLIP_Z / VISPAC K / MECH seal.
SPT CP2 & IVC TURKEY has same capacity & motor rating only seal type is different?
MPS Gear Pump Thermorex RT 180/ Thermorex RT TRT 180-5/ Thermorex TRP 180 /THERMOREX TRP 180-5/Thermorex TRP 180-HV
** ALPHAPET & EIPET PP pumps MPS Gear Pump Thermorex RT 180 are same make same capacity but different KW motor 37/30 KW.
Both have double mech seal but seal failure cost shown high in ALPHAPET but not shown in EIPET? WHY not VISPAC seal?
** MICROPET PP pump has high seal failure cost . Double mech seal ? Can change to VISPAC?

## Slide 7: OBSERVATION FOR POLYMER PUMPS
1
APT CP-2 & SPT CP1 have same capacity pumps VACOREX 180/180 & VACOREX 180-M.
Motor KW is different at APT CP_2 110 Kw & SPT CP1 is 75 KW.
To check GB details as APT has FALK & SPT has DAVID brown.
2
IVL POLAND VACOREX 280_HV has very less Motor power 132 Kw for 28 Tone /hr capacity throughput?
No other major observations as completely different combinations used at different sites .
Similar models spares parts cost is not yet benchmarked so cannot compare. We can have a comparison of all spare parts cost for these pumps and see if have some common spares.
Failures and problem faced are not mentioned by any site with these pumps.
OGP for same throughput has 315 KW motor ? While for 36 Tons per Hr EIPET has 315 Kw motor?

## Slide 8: SUMMARY AND PATH FORWARD
Pumps seals and spare parts pricing for similar models to be benchmarked and have group discounted pricing discussions with MAAG for reducing cost .
Support from MAAG for spares for pumps which are operating since 1994/96 & study upgradation possibility .
Modify /upgrade seal types to have more reliability on operation .

## Slide 9: CUTTER BENCHMARKING
CUTTER DATA
OBSERVATION
CONCLUSION AND PATH FORWARD

## Slide 10: RIETER CUTTERS AT IVL
USG 600 MODEL Total 28
** M-USG-600 H Total 2
APT CP-2 / GIVL
USG 900 MODEL Total 25
** M-USG-900 H Total 9
OGP(3)/SPT(3)/IVPM(3)

## Slide 11
CUTTERS DATA

## Slide 12
CUTTERS DATA

## Slide 13
CUTTERS DATA

## Slide 14: OBSERVATION
1
Algae treatment system
Most of the sites use treatment system except IPPI/ HALDIA/ GIVL CP-2
2
Band filter
Most of sites use 100% Polyester and 10-20µ size.
3
Dryer type
Most of sites still use AERO LINE. Energy efficient Centro Dryer used at few sites.

## Slide 15: OBSERVATION
4
Maintenance frequency( LOT OF VARIATIONS SEEN )
USG 600
USG 900

## Slide 16: REPETITIVE ISSUES FACED BY IVL SITES IN CUTTERS
IR sensor malfunction causing big lumps on cutter.
Long and thin pellets during start / running (USG 600 models).
Cutter cannot re-start at operating capacity need to reduce to 50% throughput to take in line ( USG 600 models )
Stand monitoring actuated due to overflow water distributor blocks with algae.

## Slide 17: PATH FORWARD
Cutter bearings, spares and rotor regrinding cost to be benchmarked across the sites and to be optimized. Group discounted pricing discussions with MAAG for spares .
Repetitive issue faced to be taken up with MAAG to have more reliability on operation.
Band filter paper roll cost benchmarking across sites and develop cost effective vendors .
Upgrade possibility for more energy efficient cutters/ dryers wherever possible.